## Slide 1
CHESS TECHNICAL GUIDANCE
Coastal Engineering Manual
Modernization Plan
Where EM 1110-2-1100 (drafted 1998-2008, last updated Change 3, 2011) has fallen behind
current practice, datasets, models, and standards, with a crosswalk of CEM content to
twelve cross-cutting coastal-engineering topic areas.
78 modernization items across the six Parts · high-priority items independently verified 2026-06-25

## Slide 2
VERIFICATION & METHOD
Independently fact-checked against current sources
▪ Each Part was assessed for content that has fallen behind current 2020s practice, standards, datasets, models, and guidance (the CEM was last materially updated by Change 3, 2011).
▪ Each high-priority item was then independently fact-checked (2026-06-25) against authoritative sources: USACE Publications and ERDC-CHL (Coastal Hazards System, Engineering With Nature), NOAA, USGS, FEMA, CIRIA, the EurOtop manual, and peer-reviewed literature.
Verification result
Every high-priority item was confirmed: the cited CEM content is genuinely dated, and the named modern replacement is the current standard, successor tool, or governing USACE policy. Corrections from the pass were folded in (EP 1100-2-1 in place of the superseded ETL 1100-2-1; ASCE 7-22 Chapter 5 for coastal flood loads).
How to use: the CEM remains a strong foundational reference; these items mark where to apply current USACE ERDC-CHL guidance, the Coastal Hazards System, and post-2011 circulars in design.
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
2

## Slide 3
PRIORITY SUMMARY
78 modernization items
High-priority items independently fact-checked against authoritative sources (2026-06-25).
78
items across six Parts
32
high priority
32
medium priority
14
low priority
By Part (high / medium / low):
Part I — Introduction
5 / 4 / 2
total 11
Part II — Coastal Hydrodynamics
6 / 7 / 2
total 15
Part III — Coastal Sediment Processes
5 / 5 / 3
total 13
Part IV — Coastal Geology
4 / 3 / 4
total 11
Part V — Coastal Project Planning and Design
6 / 5 / 1
total 12
Part VI — Design of Coastal Project Elements
6 / 8 / 2
total 16
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
3

## Slide 4
WHAT DRIVES THE MODERNIZATION
A few cross-cutting themes recur across all six Parts
Sea-level rise & climate adaptation
From background awareness to a required, scenario-based design input under USACE policy.
Probabilistic coastal-hazard analysis
From the Empirical Simulation Technique to JPM-OS and the Coastal Hazards System.
Process-based & spectral models
From 1D/legacy codes (GENESIS, SBEACH, WIS 1G/2G) to GenCade, XBeach, SWAN, ADCIRC.
International design standards
From the 1984 Shore Protection Manual to EurOtop (2018) and the Rock Manual.
Natural & nature-based features
From a hard-vs-soft taxonomy to NNBF and Engineering With Nature as first-class options.
Current datasets & datums
From 1929/1971-era figures to WIS hindcasts, USGS DSAS, NAVD88, and NOAA VDatum.
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
4

## Slide 5
MODERNIZATION CANDIDATES — HIGH PRIORITY (1 OF 4)
Sea-level rise & climate adaptation
I-1-3 / I-2-5 — SLR & climate absent from framing
→ USACE ER 1100-2-8162 + Sea Level Change Curve Calculator; NOAA 2022 scenarios; IPCC AR6
II-5-4 — "sea level not rising to cause undue concern"
→ Three-scenario relative sea-level-change analysis (ER 1100-2-8162, EP 1100-2-1)
III-3-3h / IV-3-5f — Bruun Rule for SLR shoreline response
→ Probabilistic / process-based: PCR model, sediment budget, XBeach / Delft3D / CMS
IV-1-6 — SLR existence, rate, and policy
→ Treat accelerating SLR as established; design the full Low / Intermediate / High envelope
V-2 / V-3 — SLR in project planning
→ Adaptive pathways and adaptation tipping points; NOAA 2022; IPCC AR6
VI-1/3/5/8 — SLR & life-cycle design basis
→ Apply ER 1100-2-8162 and EP 1100-2-1 across all design conditions
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
5

## Slide 6
MODERNIZATION CANDIDATES — HIGH PRIORITY (2 OF 4)
Probabilistic coastal-hazard, surge & wave climate
II-5-5b / II-8-5d — Empirical Simulation Technique (EST) & traditional JPM
→ JPM-OS with ADCIRC+SWAN/STWAVE storm suites; USACE Coastal Hazards System (CHS)
IV-1-5b / EM 1110-2-1412 — still-water surge / base flood elevation
→ FEMA coastal flood-hazard mapping; ADCIRC+SWAN; JPM-OS / response-surface emulators
V-1 / V-3 / V-4 — EST risk-based storm-response method
→ CHS / Probabilistic Coastal Hazard Analysis (NACCS, SACS); CSTORM-MS
V-2 — Standard Project / Probable Maximum Hurricane
→ JPM-OS + ADCIRC (STWAVE / unSWAN); hindcast & reanalysis, not single-station tables
II-2-3 — U.S. wave-climate tables (older WIS database)
→ Current WIS (wis.erdc.dren.mil) + CHS; WAVEWATCH III / WAM / SWAN production models
II-2-2 — 1G/2G hindcast models (WAVAD, WISWAVE, WAM)
→ WAVEWATCH III, WAM Cycle 4.5+, and SWAN (nearshore)
II-5-4 — NGVD 1929 vertical datums
→ NAVD88 (NATRF2022 forthcoming); NOAA VDatum; current National Tidal Datum Epoch
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
6

## Slide 7
MODERNIZATION CANDIDATES — HIGH PRIORITY (3 OF 4)
Coastal-structure design: runup, overtopping, armor, forces
I-4 — reliance on the 1984 Shore Protection Manual
→ EurOtop (2018); Rock Manual (CIRIA C683, 2007); reliability / risk-based design
II-4-4 — wave runup on beaches (Hunt 1959, Mase 1989)
→ Stockdon et al. (2006); EurOtop (2018); FEMA (2018); XBeach for complex cases
VI-5-2b (Tables VI-5-8..12) — mean wave overtopping
→ EurOtop (2018), adopted by FEMA 2023; PC-Overtopping / neural-network tools
VI-5-2a (Tables VI-5-1..7) — wave runup on slopes
→ EurOtop (2018) runup formulae and influence-factor tables
VI-5-3a (Tables VI-5-22/23) — rubble-mound armor stability
→ Rock Manual (C683); Van der Meer / Van Gent; site-specific physical model tests
VI-5-4 (Tables VI-5-53..55) — wave forces on vertical / composite walls
→ EurOtop / PROVERBS (Oumeraci et al. 2001); CFD / SPH; physical model tests
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
7

## Slide 8
MODERNIZATION CANDIDATES — HIGH PRIORITY (4 OF 4)
Sediment transport, shoreline change & nature-based features
III-2-3a — CERC / SPM bulk-energy-flux longshore transport
→ Kamphuis (2002); GenCade / CMS / Delft3D; treat CERC as order-of-magnitude with uncertainty
III-2-4b / V-3-3e — GENESIS shoreline-change model
→ GenCade v1.x in SMS with CMS-Wave / CMS-Flow; Delft3D / MIKE21 for area models
III-3-3i/k / V-4 — SBEACH cross-shore storm response
→ XBeach (non-hydrostatic) and CSHORE; couple with probabilistic storm forcing
V-3 / V-4 — coastal-armor structural design references
→ EurOtop (2018); ASCE 7-22 Ch. 5 (flood loads); FEMA Coastal Construction Manual (P-55)
I-2-5 / V-7 — hard-vs-soft solution taxonomy
→ NNBF International Guidelines (2021); Engineering With Nature; living shorelines
I-2-4 — 1971 National Shoreline Study erosion statistics
→ USGS National Assessment of Shoreline Change (DSAS); Coastal Change Hazards Portal
I-1-1 — "current state-of-the-art" self-description
→ Cross-check against current ERDC-CHL guidance, CHS, and Engineering With Nature
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
8

## Slide 9
CEM TOPIC CROSSWALK
Twelve cross-cutting topics → CEM coverage
Primary = a main subject of the chapter. Topics 1-6.
TOPIC
PRIMARY CEM COVERAGE
1
Coastal projects & hazards
V-1, V-3, V-5, V-7; I-1 / I-2; VI-2
2
Coastal measurements
V-2 Site Characterization; II-8; VI-8 Monitoring
3
Modeling data resources
II-2 (WIS hindcasts); II-3; V-2
4
Typical CE workflows
V-1 design process; VI-5; V-3 / V-4 / V-5
5
Storm-hazard probabilistic analysis
II-8 (extremal, JPM); II-5; II-2
6
Navigation structure response
VI-5 fundamentals of design; VI-2; VI-7
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
9

## Slide 10
CEM TOPIC CROSSWALK
Twelve cross-cutting topics → CEM coverage
Topics 7-12.
TOPIC
PRIMARY CEM COVERAGE
7
Navigation functional response
II-7 Harbor Hydrodynamics; V-5; II-6 Tidal Inlets
8
Flood-risk-reduction structure response
VI-5 (overtopping, runup, stability); V-3; VI-2
9
Coastal morphology
IV-2, IV-3; III-2, III-3, III-5
10
Reliability & probabilistic analysis
VI-6 Reliability-Based Design; VI-5
11
Life-cycle simulation
VI-8 Monitoring, Maintenance, Repair; VI-6
12
Integration with planning tools
V-1 (benefit-cost, decisions); V-3; V-7
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
10

## Slide 11
COVERAGE GAPS
Where the CEM is thin, even before outdatedness
Two cross-cutting capabilities are present in the CEM only as separate, mostly deterministic treatments, not as integrated frameworks. Both are natural targets for modernization.
Probabilistic life-cycle simulation
Topics 5, 10, and 11 (storm-hazard analysis, reliability, life-cycle) exist, but as separate deterministic / analytic treatments rather than one integrated stochastic life-cycle framework.
Integration with modern planning / decision-support tools
Topic 12 is process-and-economics oriented and predates current risk-informed decision platforms; the CEM does not connect its methods to them.
CHESS Technical Guidance · Coastal Engineering Manual Modernization Plan
11

## Slide 12
A foundation to build on, not to retire
▪ The CEM remains a strong foundational reference; the 78 items mark where current guidance supersedes it, and the high-priority items are independently verified.
▪ The largest, most consistent driver is sea-level rise and climate adaptation, now a required design input under USACE policy rather than background awareness.
▪ The next step is a prioritized modernization program that applies the verified replacements through current USACE ERDC-CHL guidance and the Coastal Hazards System.
Full detail, references, and per-Part tables: docs/CEM_Modernization_Plan.md